## Slide 1: IoT Extensions for schema.org
Community Teleconference
February 18, 2020

## Slide 2: Agenda
Agenda review
schema.org integration patterns
AOB

## Slide 3: Schema.org Integration
Class names Event, Action, Property conflict
iotschema has diverse semantic types for objects, schema.org has diverse property types
Property types could be synthesized from objects but…
iotschema will potentially define hundreds of types for physical quantities (temperature, humidity, voltage, acceleration…), control affordances (open/close, brightness, color control, camera controls, operating modes…), and features of interest (rooms, machines…)

## Slide 4: Schema.org Integration
The WoT use case is based on annotation consisting of RDF @type statements that point to URIs of defined terms for specialized types that conform to the classes in the meta-model
These meta-model classes would add 7 new iot types to schema.org
  iotThing, iotCapability, iotEvent, iotAction, iotProperty, iotData, iotFeatureofInterest
  new types like iotInterface as needed

## Slide 5: iotschema UML

## Slide 6: Schema.org Integration
There is a potential example pattern in schema.org
  MedicalEntity, with 7 property types
Likewise, an IoT Schema instance would contain some set of iotThing, iotCapability, iotAction, iotProperty, iotEvent, iotFeatureOfInterest classes and associated Property Types
Specialization of iot types would happen at the next level in the graph – hosted in a separate namespace
  URIs that point to accepted specialized definitions in one or more specialized namespaces
  lighting controls, thermostats, etc. that conform to the base types but have their own Property Types

## Slide 7: Application Type Example
hasSwitch
OnOffControl
providesOnOffProperty
providesTurnOnAction
providesTurnOffAction
providesToggleAction
providesOnOffStateData
providesPowerInterruptedEvent
providesPowerRestoredEvent
hasOnOffControl
OnOffProperty
TurnOnAction
OnOffStateData
Switch
PowerInterruptedEvent
schema:hasIotThing
iot:hasSwitch
iot:Switch
schema:IotThing

## Slide 8: Conclusion
Next steps/meeting
AOB

## Slide 9: Backup
Interaction model survey
Thing Class
OneDM Integration

## Slide 10: Meta-model survey – Common Affordance Semantics
Information | OneDM SDF | WoT TD | iotschema | ZCL/dotdot | OCF | SmartThings | LWM2M | Weave | Vorto | UPnP | BLE Mesh | Azure DTDL | oneM2M | OPC UA
Governing body | OneDM Liaison | W3C | W3C/schema.org | Zigbee Alliance | OCF | SmartThings | OMA SpecWorks | Google/Nest | Eclipse | OCF | BT Sig | Microsoft | oneM2M | OPC
Tools License | BSD | Many |  | Proprietary | BSD | Proprietary |  | Apache2 | Eclipse |  |  | MIT | Apache2.0 | 
Models License | BSD | No Models |  | BSD | BSD | Proprietary | OMA | Apache2 |  |  |  | CC Attr. 4.0 |  | 
representation language | JSON | LSON-LD | JSON-LD | XML | JSON | JSON | XML | WDL | vortolang | XML | XML | JSON-LD | XML | XML
Content Format | sdf+json | td+jsonld | jsonld | zcl+xml | swagger+ json | json | mod+xml | text | text | upnp+xml | xml | jsonld | sdt+xml | 
Reference | https://github.com/one-data-model/language | https://www.w3.org/TR/wot-thing-description/ | https://github.com/iot-schema-collab/iotschema | https://zigbeealliance.org/wp-content/uploads/zip/dotdot-ip-package.zip | https://openconnectivity.org/developer/specifications/ | https://docs.smartthings.com/en/latest/capabilities-reference.html | http://www.openmobilealliance.org/wp/omna/lwm2m/lwm2mregistry.html | https://openweave.io/guides/weave-primer/schema | https://github.com/eclipse/vorto/tree/development/docs | https://openconnectivity.org/developer/specifications/upnp-resources/upnp/ | https://www.bluetooth.com/specifications/mesh-specifications/ | https://github.com/Azure/IoTPlugandPlay/tree/master/DTDL | http://www.onem2m.org/tr-0039/ipe-and-sdt | https://opcfoundation.org/developer-tools/specifications-unified-architecture
Terminology | OneDM SDF | WoT TD | iotschema | ZCL/dotdot | OCF | SmartThings | LWM2M | Weave | Vorto | UPnP | BLE Mesh | Azure DTDL | oneM2M | OPC UA
Composed Instance | Thing/Thing | Thing | Thing/Thing | Device/EP | Platform/Device | Fingerprint | Registration | Device | Info Model | Device | Device | Capability Model | Device | Device, Server
Atomic Functionality Unit | Object | (Thing) | Capability | Cluster | Resource | Capability | Object | Trait | Function Block | Service | Model | Interface | ModuleClass | Object
Externalized state item | Property | Property | Property | Attribute | Property | Attribute | Resource | Property | Config, Status | State Variable | Attribute | Property | Data Point | Attribute, Variable
External method accepted | Action | Action | Action | Command | POST | Command | Executable Res. | Command | Operation | Action | Write | Command | Action | Method, Program
External signal emitted | Event | Event | Event | Report | Observe data | Device Event | Observe data | Event | Event | Event | Report | Telemetry | Event | Event, Alarm
Reusable data type | Datatype | Datatype | Datatype | Datatype | OAS definition | Datatype | Reusable Res. | Datatype | Datatype | Datatype | Datatype | schema | xsd types | register types
Network Binding | OneDM SDF | WoT TD | iotschema | ZCL/dotdot | OCF | SmartThings | LWM2M | Weave | Vorto | UPnP | BLE Mesh | Azure DTDL | oneM2M | OPC UA
Data Schema | JsonSchema | JsonSchema | External | XML | OAS 2.0 | Mapping Files | SenML | WDL | External | XML | XML | DTDL | XSD | 
Protocol Binding | External | TD Forms | External | ZCL Commands | OAS 2.0 | Device Handlers | CoAP | WDM | External | UPnP defined | BLE GATT | External | External | 
Protocols |  | MQTT,HTTP,CoAP |  | Zigbee Pro, CoAP | CoAP | Many | CoAP | WDM |  | HTTP | BLE |  |  | 

## Slide 11: Thing Class
Encapsulate reusable Capabilities
  On/Off with state Property, Commands, and Events
  Compose Air Conditioner Thing from OnOff, Mode, Speed, etc. as reusable Capabilities
Reusable compositions of Capabilities
  An Outlet unit for a multi-outlet strip
  Each Outlet has OnOff, Energy Monitor, Overcurrent and Overtemperature protection Capabilities
  Multiple Outlets are composed into an outlet strip
  Outlet unit can be a Thing
  Outlet Strip can also be a Thing

## Slide 12: ODM Meta-Model
Thing Class to compose Objects
View (Interface) Class to virtualize affordances
Reusable Objects
  Property, Action, and Event Affordances
Reusable Data Types

## Slide 13: iotschema UML with iotThing class

## Slide 14: schema.org IoT Extension Meta Model with Thing Class
schema:thing
IotCapability
InteractionPattern
IotAction
IotEvent
IotProperty
acceptsInputData
providesOutputData
providesInteractionPattern
rdfs:subclassOf
schema:Property
iotschema Class
Reused Class
IotDataItem
schema:PropertyValue
schema:PropertyValueSpec.
IotThing
hasIotThing
hasIotCapability

## Slide 15: One Data Model integration
Re-shape One Data Model definitions as iotschema definitions
One Data Model uses JSON object hierarchy vs. RDF links
  JSON pointer fragment identifiers
  st:#/sdfObject/onoff/sdfAction/turnon
iot:onoffCapability => iot:providesTurnonAction => iot:turnonAction
  iot:providesTurnonAction is a sub-class property from iot:providesInteractionPattern

## Slide 16: iotschema from OneDM
st:#/sdfObject/onoff/sdfAction/turnon
sdfObject is "sameAs" iotCapability
Create type names
  st:#/sdfObject/switch => iot:switchCapability
  st:#/sdfObject/switch/sdfAction/turnon => iot:turnOnAction (iot:switchTurnOnAction?)
Synthesize the schema.org style property types
  providesInteractionPattern subtypes
  providesSwitchTurnOnAction

## Slide 17: Path Construct in RDF
st:#/sdfObject/onoff/sdfAction/turnon
  "@id": "iot:iotCapability/onoff"
  "@id": "iot:iotCapability/onoff/iotAction/turnon"
What does the property type look like?
  iot:providesInteractionPattern
  iot:providesTurnonAction
  iot:providesiotCapability/onoff/iotAction/turnon